## Slide 1: Micro-Architecture Optimization on single-issue 5-stage RISC-V processor
Kei Hong Chan
Yiu Fai Lam

## Slide 2: Overview
Data forwarding
Branch instruction
Eliminate jump stall
Load Store extension
Performance evaluation

## Slide 4: Branch instruction
Introduce BHR and PHT
Extra module to control the MUX in IF stage
Load Branch dependency check

## Slide 5: BHR_and_PHT
Input: ID_PC, ID_opcode, ID_func3, zero_signal
Output: PHT_out
4-bit is used for global Branch History Register (BHR)
PHT has 128 entries, 2-bit Branch Predictor with Saturating Up/Down scheme
PHT address is the combination of bit 2 to bit 4 of PC and 4-bit global BHR

## Slide 6: IF_MUX_sel
Input: inst_in, ID_opcode, ID_func3, PHT_in, zero_signal
Output: big_mux_sel, small_mux1_sel, small_mux2_sel, flush_signal
control the MUX in IF stage, select calculated PC value to update
Prediction wrong => flush_signal = 1
When flush_signal = 1:
flush the PC value
flush the instruction stored in IF/ID register
send a NOP instruction to ID stage

## Slide 7: Connection of MUX in IF stage (before adding “IF_MUX_sel” module)

## Slide 8: Connection of MUX in IF stage (after adding “IF_MUX_sel” module)

## Slide 9: branch_load_check
Input: inst_in, IF_ID_inst_in
Output: branch_load_dstall
check the dependency between branch and load instruction
If dependency occurs => branch_load_dstall = 1
When branch_load_dstall = 1:
Hold PC value
send a NOP instruction to ID stage

## Slide 10: Eliminate jump stall
Original: an extra stall for jump instruction to execute in ID stage
Optimized: 0 stall, still execute in ID stage but pass the latest PC value to IMEM and IF/ID resigter directly
Extra MUX in IF stage is needed, control by controller

## Slide 11: Connection of MUX in IF stage (before eliminate jump stall)

## Slide 12: Connection of MUX in IF stage (after eliminate jump stall)

## Slide 13: Load_extend
Input: RAM_data_in, EXE_MEM_LOAD_type, EXE_MEM_LOAD_sign
Output: data_in
Placed in MEM stage
Extend the RAM data after read it from RAM
Pass the extended data to MEM/WB register
Support LW, LH, LB, LHU, LBU instruction

## Slide 14: Store_extend
Input: ID_EXE_Data_out_2, ID_EXE_STORE_type
Output: ID_EXE_Data_extended
Placed in EXE stage
Extend the data after data forwarded for store instruction
Pass the extended data to EXE/MEM register
Support SW, SH, SB instruction

## Slide 15: Performance evaluation
Test program type | original processor execution time | optimized processor execution time | Speeded up (optimized vs original)
data dependency + branch + jump | 1110 clock cycle | 609 clock cycle | 1.823 times faster than original processor
branch + jump | 913 clock cycle | 814 clock cycle | 1.122 times faster than original processor
Each program execute with a simple for loop, with 100 iterations
1st test program is faster than original processor
2nd test program is faster than original processor

## Slide 16: Instruction code for performance evaluation
data dependency + branch + jump
branch + jump